## Slide 1
🔒
TEAM-02 · FCDF-COHORT-11 · LEVEL 1, SEMESTER 1
TCP/IP Communication
Tracing a Secure HTTPS Website Request Across the Network
Application Layer
Transport Layer
Internet Layer
Network Access Layer
Presented by
Abdul Fatawu Umar
2026/FCDF/16899
Maryjudith Chidinma Ogunaka
C11/26/FCDF/17151
Scenario: Opening a Secure Website (HTTPS)

## Slide 2
FOUNDATIONS
What Is the TCP/IP Model?
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
1 / 12
TCP/IP (Transmission Control Protocol / Internet Protocol) is the rule set that governs how devices communicate over the Internet.
It organizes communication into four layers, each with a distinct job — from generating a request to placing bits on the wire.
Every online activity — browsing, email, video calls, file transfer — depends on all four layers working together.
Our scenario (opening a secure website) exercises every layer, which is why it is a good vehicle for explaining the model.
Application Layer
Data
Transport Layer
Segments
Internet Layer
Packets
Network Access Layer
Frames / Bits
Closest to the user
Closest to the wire

## Slide 3
SCENARIO
Selected Scenario: Opening a Secure Website
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
2 / 12
User action: Typing https://www.amazon.com into a browser and loading the page over a secured HTTPS connection.
The user's browser resolves the site's name and opens a secure (encrypted) connection to the web server.
The request and response pass down through all four TCP/IP layers on the client and back up through all four on the server.
This single request touches addressing (IP), delivery (TCP ports), routing (routers), and physical transmission (Wi-Fi/Ethernet) — making it ideal for showing the whole model end to end.
We trace it step by step in the following slides: application → transport → internet → network access → across the Internet → and back.
👤
User
🖥
Browser
📡
Home Router
🌐
ISP Network
🗄
Web Server

## Slide 4
LAYER 1 OF 4
Application Layer — Starting the Request
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
3 / 12
APPLICATION LAYER
Function: generates the user-facing request and interprets the response — the only layer users directly interact with.
Key protocols: HTTPS/HTTP (web pages), DNS (name resolution), TLS (encryption for HTTPS).
DNS first resolves www.amazon.com to an IP address; then the browser builds an HTTPS request.
Destination port: 443 (HTTPS) is the well-known port the server listens on for secure web traffic.
Sample request generated
GET / HTTP/1.1
Host: www.amazon.com
Destination Port: 443 (HTTPS)
🔒
Why HTTPS, not HTTP?
TLS encrypts the request before it ever leaves the Application Layer, protecting it from eavesdropping further down the stack.

## Slide 5
LAYER 2 OF 4
Transport Layer — TCP Segmentation & Handshake
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
4 / 12
TRANSPORT LAYER
Function: breaks application data into segments, adds port numbers, and guarantees reliable, ordered, error-checked delivery.
Protocol used here: TCP (Transmission Control Protocol) — chosen because HTTPS needs guaranteed, in-order delivery.
Port numbers: source = a random ephemeral port (e.g. 51322) on the client; destination = well-known port 443 on the server.
Before any data moves, TCP opens the connection with a three-way handshake.
Client
Server
SYN (port 51322 → 443)
SYN-ACK (443 → 51322)
ACK — connection established
Once established, the client's HTTPS request is sent as one or more TCP segments.

## Slide 6
LAYER 3 OF 4
Internet Layer — IP Addressing & Routing
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
5 / 12
INTERNET LAYER
Function: wraps each segment in an IP packet, adds source and destination IP addresses, and routes the packet toward the destination.
Protocol used: IP (Internet Protocol) — acts like a postal address system for the network.
Routers examine the destination IP address and forward the packet along the best available path, hop by hop.
The same source/destination IP pair is used for both the request and the reply, so the server's response can find its way back.
Source IP (client):
192.168.1.10
Destination IP (server):
54.239.28.85
🖥
Client
🔀
Home Router
🔀
ISP Router
🗄
Web Server
Packets are routed hop by hop using the destination IP address.

## Slide 7
LAYER 4 OF 4
Network Access Layer — Physical Transmission
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
6 / 12
NETWORK ACCESS LAYER
Function: wraps the IP packet in a frame and physically transmits bits across a medium — Wi-Fi, Ethernet cable, or fibre.
Uses MAC addresses — physical hardware addresses — to move the frame to the next device on the local network (e.g., the router).
Network devices involved: network interface card (NIC), Wi-Fi access point / switch, and the router's local interface.
This is the only layer that touches the physical medium — every layer above it is logical.
🖥
Laptop (NIC)
MAC: A4:5E:60:11:22:33
📶
Wi-Fi Access Point
802.11 wireless link
🔀
Router / Switch
Forwards frame onward

## Slide 8
DATA JOURNEY
Encapsulation & Decapsulation
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
7 / 12
As data descends the client's stack, each layer adds its own header (encapsulation). The server reverses the process on receipt (decapsulation).
Data
Segment (+TCP header)
Packet (+IP header)
Frame (+MAC header) → Bits
ENCAPSULATION (sender, top → bottom)
PROTOCOL ANALYSIS TABLE
Layer | Protocol | PDU | Addressing | Purpose
Application | HTTPS/DNS/TLS | Data | URL / domain name | Build & encrypt request
Transport | TCP | Segment | Port 443 / ephemeral | Reliable, ordered delivery
Internet | IP | Packet | Source / dest. IP | Logical addressing & routing
Network Access | Ethernet / Wi-Fi | Frame | Source / dest. MAC | Physical transmission
DECAPSULATION (receiver, bottom → top)
The web server receives bits, reassembles the frame, strips the MAC header, passes the packet up and strips the IP header, reassembles TCP segments and strips the TCP header, then hands the raw HTTPS request to the web application.

## Slide 9
MODEL COMPARISON
Mapping TCP/IP to the OSI Model
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
8 / 12
The 4-layer TCP/IP model is a practical, condensed version of the 7-layer OSI reference model.
TCP/IP Layer | Corresponding OSI Layer(s) | Example in Our Scenario
Application | Application, Presentation, Session | Browser builds HTTPS request; TLS session negotiated
Transport | Transport | TCP segments data; ports 443 / ephemeral used
Internet | Network | IP addresses attached; router forwards packet
Network Access | Data Link, Physical | Frame built with MAC address; bits sent over Wi-Fi
Note: OSI is a conceptual 7-layer reference model; TCP/IP is the practical 4-layer model actually implemented on the Internet.

## Slide 10
TRANSPORT CHOICES
TCP vs UDP — Choosing the Right Protocol
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
9 / 12
TCP
Transmission Control Protocol
Connection type
Connection-oriented (handshake first)
Reliability
Guaranteed delivery, with retransmission
Ordering
Data arrives in the order it was sent
Speed
Slower — overhead from reliability checks
Header size
20 bytes (larger)
Used by our scenario for
HTTPS web request (port 443)
Other examples
Email (SMTP), file transfer (FTP)
UDP
User Datagram Protocol
Connection type
Connectionless (no handshake)
Reliability
Best-effort — no delivery guarantee
Ordering
No guaranteed order
Speed
Faster — minimal overhead
Header size
8 bytes (smaller)
Not used here because
HTTPS needs guaranteed, ordered delivery
Typical examples
Video streaming, VoIP calls, online gaming, DNS queries

## Slide 11
ORIGINAL DIAGRAM
Complete Packet Journey — Request & Response
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
10 / 12
CLIENT (Browser)
Application
Transport
Internet
Network Access
WEB SERVER
Application
Transport
Internet
Network Access
INTERNET
→ HTTPS request (encrypted)
← HTTPS response (encrypted page)
Data travels down the client's stack, across the Internet, and up the server's stack for the request — then the reverse path returns the response.

## Slide 12
DIAGNOSTICS
Troubleshooting a Communication Failure
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
11 / 12
Failure scenario: The user's browser shows “This site can’t be reached” when opening https://www.amazon.com.
1
Confirm physical connectivity
Network Access
Check Wi-Fi/Ethernet link light and adapter status; retry on another network if needed.
2
Verify IP configuration
Internet
Run ipconfig / ifconfig and ping the default gateway to confirm the device has a valid IP.
3
Test DNS resolution
Application
Run nslookup www.amazon.com — failure here means the name isn’t resolving to an IP.
4
Check port & firewall
Transport
Confirm port 443 isn’t blocked by a local firewall or the ISP; test with telnet/Test-NetConnection.
5
Inspect the TCP handshake
Transport
Capture traffic (e.g., Wireshark) to see if SYN/SYN-ACK/ACK completes; an incomplete handshake points to a network path issue.
6
Validate the TLS certificate
Application
If the handshake completes but HTTPS fails, check for an expired/invalid certificate on the server.

## Slide 13
CONCLUSION
Key Takeaways
TCP/IP’s four layers each add a specific header, enabling reliable end-to-end communication.
Ports (443/ephemeral) and IP/MAC addresses together get data to the right application on the right device.
TCP trades speed for reliability — the right choice for HTTPS; UDP trades reliability for speed — right for streaming, VoIP, gaming and DNS.
The OSI model maps cleanly onto TCP/IP and gives a more detailed vocabulary for the same process.
A layer-by-layer troubleshooting approach (physical → IP → DNS → port → handshake → TLS) isolates failures quickly.
Application
Transport
Internet
Network Access
Thank you — Questions?
TEAM-02 · TCP/IP Communication in Action · FCDF-COHORT-11
12 / 12

## Slide 14
APPENDIX · NOT COUNTED IN 12 CONTENT SLIDES
Team Contribution Record
Member | Slides Presented | Contribution
Maryjudith Chidinma Ogunaka C11/26/FCDF/17151 | Slides 1 - 7 | Presented the title, introduction to the TCP/IP model, the selected scenario, and the Application, Transport, Internet and Network Access layers.
Abdul Fatawu Umar 2026/FCDF/16899 | Slides 8 - 13 | Presented encapsulation & decapsulation, the OSI mapping, TCP vs UDP comparison, the packet journey diagram, troubleshooting, and the conclusion.

## Slide 15
REFERENCES · NOT COUNTED IN 12 CONTENT SLIDES
References
1
RFC 9293 — Transmission Control Protocol (TCP)
IETF · Official Internet standard defining TCP.
www.rfc-editor.org/rfc/rfc9293
2
Introduction to Networks — The OSI and TCP/IP Models
Cisco Networking Academy · Recognised vendor networking-academy course material.
www.netacad.com
3
What Happens When You Type a URL Into Your Browser?
Cloudflare Learning Center · Vendor explainer on the request/response journey.
www.cloudflare.com/learning
4
An Overview of HTTP
MDN Web Docs (Mozilla) · Reference documentation on HTTP/HTTPS.
developer.mozilla.org